## Slide 1
ARCHITECTURE OF 8086

## Slide 6
ADDRESSING MODES

## Slide 9
MINIMUM MODE AND TIMING DIAGRAM

## Slide 12
I/O WRITE
I/O READ

## Slide 13
MEMORY READ
MEMORY WRITE

## Slide 14
INTERRUPTS

## Slide 19
RISC is a design philosophy aimed at delivering simple but powerful instructions that execute within a single cycle at a high clock speed
RISC philosophy is implemented with four major design rules
Instructions — RISC processors have a reduced number of instruction classes.
These classes provide simple operations that can each execute in
single cycle
Pipelines — The processing of instructions is broken down into smaller units that can be executed in parallel by pipelines
Registers — RISC machines have a large general-purpose register set. Any register can contain either data or an address
Load-store architecture — The processor operates on data held in registers.
Separate load and store instructions transfer data between the register bank and external memory
RISC DESIGN PHILOSOPHY

## Slide 20
ARM DESIGN PHILOSOPHY
ARM processor has been speciﬁcally designed to be small to reduce power consumption and extend battery operation
Single-chip solution, the smaller the area used by the embedded processor, more available space for specialized peripherals.
High code density
Incorporated hardware debug technology
ARM core is not a pure RISC architecture because instruction set differs from the pure RISC
Variable cycle execution for certain instructions
Inline barrel shifter leading to more complex instructions
Thumb 16-bit instruction set
Enhanced instructions (DSP Functions)