## Slide 1: ECE201R01 : Microprocessor & Microcontroller Unit II: 8086 Addressing Modes

## Slide 2: Instruction Format
An instruction specifies:
  type of operation,
  location of operands
  location to store the result of the operation
Location of operands
  register name
  memory location
  immediate data

## Slide 3: Instruction Format
operand address specifies the location of operand

## Slide 4
Operands located in memory: their addresses may be specified directly or through an indirect way
Addressing Mode bits specify the operand location and how to determine the address of the operand in memory
Simplest type of instruction format contains only the Operation Code but no operand address or addressing mode bits
Instruction Format

## Slide 5: Addressing Modes
Addressing mode specifies:
  Where the operand is located
  How to reach the operand location
Operand may be located as:
  Immediate data as part of the instruction
  Data stored in one of the registers
  Data stored in memory

## Slide 6: Addressing Modes
Immediate addressing mode: data is specified as part of the instruction
  Ex: MOV BX, 97F0H (in Intel 8086)
  BX = 97F0H
Register addressing mode: operand is located in one of the registers. Name of the register in coded form may be specified in the operation code
  Ex: ADD AX, BX (in Intel 8086)
  Operand1 = Data in AX
  Operand2 = Data in BX
  AX = Operand1 + Operand2
  AX = AX + BX
Notes: BX=97F0H
AX = AX + BX

## Slide 7
Memory addressing modes: a data byte/word is located in memory. Address needs to be determined to access the data and to perform the specified operation
Address of the operand may be:
  specified directly in the instruction:
  offset address of the operand is given as a part of instruction
  given indirectly in the instruction.
  name of the register containing the offset address
  of the operand is given as a part of instruction
Addressing Modes

## Slide 8
Direct addressing mode: memory operand address (offset) is specified as part of the instruction
  Ex: OR AL, [2507H] (in Intel 8086)
  Operand1 = Data in AL
  Operand2 = Data in PA where, PA = (DS*10H) + 2507H
  AL = Operand1 | Operand2
Indirect addressing mode: the instruction specifies a register where the operand address is stored
  Ex: SUB AL, [BX] (in Intel 8086)
  Operand1 = Data in AL
  Operand2 = Data in PA where, PA = (DS*10H) + BX
  AL = Operand1 - Operand2
Addressing Modes
Notes: AL = AL – [BX]
PA = (DS*10H)+BX = 20004H
MOV AX,[BX]

## Slide 9: Addressing Modes
BASED INDIRECT: BX / BP – BASED
INDEXED INDIRECT: SI / DI – INDEXED
Based Indexed addressing mode: useful when different elements of a list or an array are to be accessed in loop for performing the same set of operations
  Base of the array is specified in a register called Base register.
  The index or distance of the element from the base of the array to be accessed is specified in a register called Index register.
  MOV [BX + DI], AL (in Intel 8086) :
  EA = [BASED] + [INDEX]
  ((DS*10H) + (BX) + (DI)) (AL)
Notes: BASED INDIRECT: BX / BP – BASED
INDEXED INDIRECT: SI / DI – INDEXED
BASED + INDEXED: EA = [BASED] + [INDEX]

## Slide 10: Addressing Modes
BASE + RELATIVE : MOV [BX+09],DL
INDEX + RELATIVE : ADD AL,[SI+78H]
Base plus Index plus Relative Addressing mode: useful in case of two-dimensional arrays
  Base register contains the base address of the array.
  Index register contains the increment from base to the row where the data is stored.
  Displacement mentioned in the instruction (immediate) or in a separate register is the displacement of the element from the start of the row.
  MOV (BX + DI + 4), CL (in Intel 8086):
  EA = [BASE] + [INDEX] + RELATIVE
  ((DS)*10H + (BX) + (DI) + 4) (CL)
Notes: EA = [BASE] + [INDEX] + RELATIVE
BASE + RELATIVE : MOV [BX+09],DL
INDEX + RELATIVE : ADD AL,[SI+78H]

## Slide 11: Addressing Modes
Notes: MOV AL, [BX+05] : AL = ((DS*10H)+BX+05) ; MEMORY READ
MOV [BX+05], AL : ((DS*10H)+BX+05) = AL; MEMORY WRITE
MOV AL, [SI+05] : AL = ((DS*10H)+SI+05)
MOV AL, [BX+SI+05] : : AL = ((DS*10H)+BX+SI+05)

## Slide 12: Thank you . . .