## Slide 1: ECE201R01 : Microprocessor & Microcontroller Unit II: 8086 Instruction Set

## Slide 2: Operands
Immediate (8-bit): 00 – FFH
Immediate (16-bit): 0000 – FFFFH
Register (8-bit): AL, AH, BL, BH, CL, CH, DL, DH
Register (16-bit): AX, BX, CX, DX, SI, DI, BP, SP
Memory Direct Address (16-bit EA): 0000 – FFFFH
Memory Indirect Address (Pointer for DS): BX, BP, SI, DI
SREG: CS, DS, SS, ES

## Slide 3: Data Transfer Instructions
Mnemonic | Operation | Operand
MOV | Copy data from Source to Destination Note: The term Memory as operand supports both DIRECT & INDIRECT The following are NOT SUPPORTED in 8086 Both operands CANNOT be Memory Immediate operand cannot be a Destination | REG, REG REG, Immediate REG, Memory Memory, REG Memory, Immediate SREG, Memory Memory, SREG REG, SREG SREG, REG
The MOV instruction cannot:
set the value of the CS and IP registers.
copy value of one segment register to another segment register
(should copy to general register first).
copy immediate value to segment register
(should copy to general register first).
Notes: ADD AL, [2000H]
SUB AL,BL ;AL=AL-BL
CMP AL,BL ; ZF==1, EQUAL (AL==BL) ;CF==1, LOWER (AL<BL) ;ZF==0 & CF==0, GREATER (AL>BL)

## Slide 4: ALU Instructions
Mnemonic | Operation | Operand
ADD | operand1 = operand1 + operand2 | REG, Memory Memory, REG REG, REG Memory, Immediate REG, Immediate
ADC | operand1 = operand1 + operand2 + CF | 
AND | operand1 = operand1 & operand2 | 
OR | operand1 = operand1 ¦ operand2 | 
XOR | operand1 = operand1 ^ operand2 | 
SUB | operand1 = operand1 - operand2 | 
SBB | operand1 = operand1 - operand2 - CF | 
CMP | operand1 - operand2 result is not stored anywhere, flags are set (OF, SF, ZF, AF, PF, CF) according to result. | 
TEST | operand1 & operand2 result is not stored anywhere, flags are set (OF, SF, ZF, AF, PF, CF) according to result. | 
Notes: ADD AL, [2000H]
SUB AL,BL ;AL=AL-BL
CMP AL,BL ; ZF==1, EQUAL (AL==BL) ;CF==1, LOWER (AL<BL) ;ZF==0 & CF==0, GREATER (AL>BL)

## Slide 5: ALU Instructions
Mnemonic | Operation | Operand
INC | operand = operand + 1 CF - unchanged! | REG / Memory
DEC | operand = operand – 1 CF - unchanged! | 
NOT | operand = ~operand Invert each bit of the operand. | 
NEG | operand = (~operand) + 1 Invert all bits of the operand then Add 1 to inverted operand | 
MUL | when operand is a byte: AX = AL * operand. when operand is a word: (DX AX) = AX * operand. | 
DIV | when operand is a byte: (Quotient) AL = AX / operand (Remainder) AH = (modulus) AX / operand when operand is a word: (Quotient) AX = (DX AX) / operand (Remainder) DX = (modulus) (DX AX) / operand | 
Notes: A=A+1; ADD AL,1 A=A-1; SUB AL,1 INC [2000H] NEG AL = NOT AL; INC AL;
A++; INC AL A--; DEC AL
MUL BL ; AX = AL * BL MUL SI ; DX:AX = AX * SI
DIV BL ; AX / BL (AX=1234H, BL=45H DIV DI ; (DX:AX) / DI

## Slide 6: Implicit Instructions
Mnemonic | Operation | Operand
CLC | CF = 0 | No operands
CLD | DF = 0 | 
CLI | IF = 0 | 
STC | CF = 1 | 
STD | DF = 1 | 
STI | IF = 1 | 
CMC | if CF = 1 then CF = 0 if CF = 0 then CF = 1 | 
NOP | Do nothing | 

## Slide 7: Branching Instructions
Mnemonic | Operation | Operand
JMP | Near: intra-segment (EA = Disp16) IP = EA Far: intersegment (BA:EA = Disp32) CS = BA, IP = EA | Target
CALL | Pushes IP to Stack then IP = EA Near: intra-segment (EA = Disp16) Pushes CS:IP to Stack then CS = BA, IP = EA Far: intersegment (BA:EA = Disp32) | 
RET | Near: Pops TOS to IP Far: Pops TOS to IP & CS | -
JC | If CF = 1, Short Jump: EA = IP + Disp8 | Disp8 -128 TO +127 (80H TO FFH) (0 TO 7FH)
JNC | If CF = 0, Short Jump: EA = IP + Disp8 | 
JZ / JE | If ZF = 1, Short Jump: EA = IP + Disp8 | 
JNZ / JNE | If ZF = 0, Short Jump: EA = IP + Disp8 | 
LOOP | Decrease CX, jump to label if CX not zero | 
Notes: -128 TO +127 : DISP8 (0 TO 7FH) (80H TO FFH) LIFO
FF H = (-1) 0000 0001 = (1s COMP) 1111 1110 = (2s COMP) = 1111 1111
80 H = (-128)
LOOP L1 = DEC CX , JNZ L1

## Slide 8: Shift & Rotate Instructions
ROR
ROL
RCL
SHR
Memory, Immediate REG, Immediate
RCR
SHL
SAR
Memory, CL REG, CL
Notes: AL = 01H = 0000 0001 ROR AL,1 = 1000 0000 = 80H
0FH = 0000 1111 SAR used to divide Signed value by 2 << >>

## Slide 9: Thank you . . .